## Slide 1
JOHANNES GUTENBERG UNIVERSITÄT MAINZ · INSTITUTE OF GEOSCIENCES
Data-Driven Stokes Flow Prediction
in Multi-Crystal Sedimentation
A Systematic Comparison of Spatial and Spectral Neural Surrogate Architectures
Paul Baselt
M.Sc. Computational Sciences
Supervisors: Prof. Dr. Boris J. P. Kaus · Prof. Dr. Michael Wand
Mainz, April 2026

## Slide 2
Agenda
01
Motivation & Research Question
02
Physical Background
03
Methodology & Architectures
04
Experiments & Results
05
Discussion & Conclusion

## Slide 3
01 — Motivation & Research Question
Why Do We Need Surrogate Models for Crystal Sedimentation?

## Slide 4
Geoscientific Context
The Problem
Crystals sediment in viscous magma fluids. This process controls the chemical differentiation of magma reservoirs.
The Numerical Challenge
Simultaneous resolution of:
Microscopic boundary layers around individual crystals
Long-range hydrodynamic interactions
~O(N²)
Scaling of
interaction costs
256×256
Simulation grid
(LaMEM)
Stokes
Regime: Re ≪ 1
[ Figure: Crystal sedimentation in magma – image to follow ]

## Slide 5
Research Question & Hypotheses
Can data-driven surrogate models replace high-accuracy Stokes solvers for flow field prediction in multi-crystal sedimentation — and which architecture generalizes better?
Three Hypotheses:
H1 Sufficient sampling of the configuration space enables OOD generalization.
H2 Predicting the stream function ψ (instead of velocity components) reduces task complexity and enforces incompressibility by construction.
H3 The FNO outperforms the U-Net, as its global receptive field is better suited for elliptic Stokes equations.

## Slide 6
02 — Physical Background
Stokes Flow & Stream Function Formulation

## Slide 7
Incompressible Stokes Flow & Stream Function ψ
Stokes Equations (Re ≪ 1)
−∇p + η∇²u = 0
∇ · u = 0
Stream Function ψ
ux = ∂ψ/∂z, uz = −∂ψ/∂x
Poisson: ∇²ψ = −ω
Advantages of the ψ-Formulation
Incompressibility guaranteed by construction (∇·u ≡ 0 for arbitrary ψ)
No penalty term required in the loss function
Scalar problem instead of vector regression
Divergence-RMS ≈ 10⁻²⁶ (confirmed by experiments)

## Slide 8
03 — Methodology & Architectures
U-Net vs. Fourier Neural Operator on identical data

## Slide 9
Methodological Workflow
LaMEM
Simulation
Stokes Solver
256×256 FD Grid
Poisson Solve
ψ-Reconstruction
∇²ψ = −ω
Dirichlet BCs
4-Channel
Input
Mask, SDF,
x/z-coordinates
Model
(U-Net / FNO)
Prediction ψ̂
Evaluation
Metrics
rel. L², MAE,
Divergence
Input Encoding (4 Channels):
Crystal mask — binary occupancy
Signed Distance Field — distance to nearest crystal surface
Norm. x-coordinate — spatial position
Norm. z-coordinate — spatial position

## Slide 10
Architecture Comparison: U-Net vs. FNO
U-Net
Encoder–Decoder + Skip-Connections
Local convolutions → hierarchical features
Batch Normalization (→ unstable training dynamics)
Checkerboard artifacts avoided (Resize-Conv)
Composite Loss: MSE + Gradient Penalty
FNO
Fourier layers + local 1×1 bypass
Global receptive field per layer (kmax = 16)
No Batch Normalization → stable dynamics
GELU activation, weights: σ = 0.02
MSE loss (no gradient term needed)
Identical data · Identical evaluation metrics · Same input encoding

## Slide 11
04 — Experiments & Results
Four Experiments — from Single Crystal to Size Generalization

## Slide 12
Experimental Design (4 Experiments)
Exp 1
Single-Crystal Baseline
n = 1, Hyperparameter Sweep
lr ∈ {10⁻³, 5×10⁻³, 10⁻⁴, 5×10⁻⁴} × bs ∈ {8, 16}
Exp 2
Multi-Crystal Generalization
Training: n ∈ {1…10}
OOD-Test: n ∈ {15, 20, 30}
Exp 3
Generalization Stress Test
Training: n ∈ {1…25}
OOD-Test: n = 50
Exp 4
Crystal Size Generalization
Training: r = 0.05 (fixed)
OOD Test: r = 0.005 (small) and r = 0.5 (large)

## Slide 13
Exp. 1: Single-Crystal Baseline — Results
FNO
Rel. L² Error on ψ
1.6 – 2.3 %
Rel. L² Error on vel.
~3 – 5 %
Monotone convergence across all configurations
U-Net
Rel. L² Error on ψ
5.5 – 6.5 %
Rel. L² Error on vel.
~11 – 13 %
Validation loss oscillations at high lrs + bs 16
Composite Loss (MSE + Gradient Penalty) reduces U-Net velocity error from ~3× to ~1.5–2× relative to ψ error

## Slide 14
Exp. 2 & 3: Multi-Crystal Generalization
Mean rel. L² Error on ψ
Experiment | FNO (in-dist) | U-Net (in-dist) | FNO (OOD) | U-Net (OOD)
Exp 2 (n ≤ 10) | ~4 – 7 % | ~17 – 29 % | ~10 % @ n=20 | ~29 % @ n=20
Exp 3 (n ≤ 25) | ~6.8 % | ~23 % | 12.4 % @ n=50 | 21.5 % @ n=50
Key Findings:
FNO consistently outperforms U-Net in-distribution by a factor of 3–4×
OOD generalization: error > 10 % at n ≈ 1.2–1.5× the training maximum (FNO)
Breadth of training distribution is the decisive factor for OOD reach
U-Net: flatter error profile across crystal counts, but worse absolute accuracy

## Slide 15
Exp. 4: Crystal Size Generalization — Rank Reversal
Small Crystals r = 0.005
FNO ψ-Error
12.1 ± 6.4 %
U-Net ψ-Error
~12 %
Both comparable
Large Crystals r = 0.5
FNO ψ-Error
71.3 ± 4.8 %
U-Net ψ-Error
44.9 ± 8.2 %
FNO fails — U-Net wins!
Variable-radius FNO (r ∈ {0.02, 0.05, 0.08}): Error reduced to 10.4 ± 10.8 % — spectral limitation overcome without architecture changes!

## Slide 16
05 — Discussion & Conclusion
Architecture Comparison · Limitations · Outlook

## Slide 17
Discussion: Causes & Implications
FNO Stability vs. U-Net Oscillations
Batch Normalization in U-Net increases the effective learning rate spread (Mehmeti-Göpel & Wand, ICML 2024) → higher sensitivity to lr and bs. FNO without BN converges monotonically.
Spectral Truncation kmax = 16
Responsible for FNO failure on large crystals: boundary layer structures require higher Fourier frequencies. Solution: training variation breadth or adaptive Fourier modes.
Stream Function as a Physically Motivated Inductive Bias
ψ-prediction guarantees exact incompressibility (Div-RMS ≈ 10⁻²⁶). No soft penalty needed — in contrast to direct velocity prediction.
Velocity Error > ψ-Error
Numerical differentiation ψ → u amplifies high-frequency residuals. Ratio: FNO ~2×, U-Net without Composite Loss ~3×, with Composite Loss ~1.5–2×.

## Slide 18
Conclusion & Answers to the Research Questions
H1 — Confirmed (for FNO)
Sufficient sampling + broad training distribution enable OOD generalization. U-Net only weakly confirmed.
H2 — Confirmed
ψ-formulation reduces task complexity and guarantees exact incompressibility for all predictions.
H3 — Conditionally Confirmed
FNO dominates in crystal count generalization. Rank reversal in size-OOD (Exp. 4): U-Net better for large crystals.
Practical Guidelines
Prefer FNO when generalization across crystal counts matters
U-Net when robustness to geometric scaling is required
Variable training data > architecture change for size generalization
Always prefer stream function over direct velocity prediction

## Slide 19
Outlook
→
Adaptive Fourier Modes
Geo-FNO or multi-resolution architectures for robust size generalization without discrete training radii
→
Hybrid Architectures (U-FNO)
Combination of local U-Net processing + global spectral layers (Wen et al. 2022)
→
Extension to 3D & Time-Dependent Flows
Realistic geophysical applications require 3D and transient Stokes flows
→
Coupled Time-Step Framework
Surrogate as building block for long-term sedimentation simulations (O(ms) instead of O(8s) per step)
→
Uncertainty Quantification
Bayesian extensions or ensemble approaches for prediction confidence

## Slide 20
Thank You!
I look forward to your questions.
4
Experiments
FNO
Dominant (Exp 1–3)
10⁻²⁶
Divergence-RMS
3–4×
FNO vs U-Net Advantage
Paul Baselt · M.Sc. Computational Sciences · JGU Mainz · April 2026
Code: gitlab.rlp.net/pbaselt/Masterarbeit_Anhang